Transoceanic Flight

602.39 No pilot-in-command of a single-engined aircraft, or of a multi-engined aircraft that would be unable to maintain flight in the event of the failure of any engine, shall commence a flight that will leave Canadian Domestic Airspace and enter airspace over the high seas unless

(a) the pilot-in-command holds a pilot licence endorsed with an instrument rating;

(b) the aircraft is equipped with

(i) the equipment referred to in 605.18

(ii) a high frequency radio capable of transmitting and receiving on a minimum of two appropriate international air-ground general purpose frequencies, and

(iii) hypothermia protection for each person on board; and

(c) the aircraft carries sufficient fuel to meet the requirements of 602.88 and, in addition, carries contingency fuel equal to at least 10 per cent of the fuel required pursuant to 602.88 to complete the flight to the aerodrome of destination.

[ this part is for Canadian aircraft, but it's worth considering. ]

Survival Equipment - Flights over Land

602.61 (1) Subject to subsection (2), no person shall operate an aircraft over land unless there is carried on board survival equipment, sufficient for the survival on the ground of each person on board, given the geographical area, the season of the year and anticipated seasonal climatic variations, that provides the means for

(a) starting a fire;

(b) providing shelter;

(c) providing or purifying water; and

(d) visually signalling distress.

(2) Subsection (1) does not apply in respect of

(a) a balloon, a glider, a hang glider, a gyroplane or an ultra-light aeroplane;

(b) an aircraft that is operated within 25 nautical miles of the aerodrome of departure and that has the capability of radiocommunication with a surface-based radio station for the duration of the flight;

(c) a multi-engined aircraft that is operated south of 66° 30' north latitude

(i) in IFR flight within controlled airspace, or

(ii) along designated air routes;

(d) an aircraft that is operated by an air operator, where the aircraft is equipped with equipment specified in the air operator's company operations manual, but not with the equipment required by subsection (1); or

(e) an aircraft that is operated in a geographical area where and at a time of year when the survival of the persons on board is not jeopardized.

Life Preservers and Flotation Devices

602.62 (1) No person shall conduct a take-off or a landing on water in an aircraft or operate an aircraft over water beyond a point where the aircraft could reach shore in the event of an engine failure, unless a life preserver, individual flotation device or personal flotation device is carried for each person on board.

(2) No person shall operate a land aeroplane, gyroplane, helicopter or airship at more than 50 nautical miles from shore unless a life preserver is carried for each person on board.

(3) No person shall operate a balloon at more than two nautical miles from shore unless a life preserver, individual flotation device or personal flotation device is carried for each person on board.

(4) For aircraft other than balloons, every life preserver, individual flotation device and personal flotation device referred to in this section shall be stowed in a position that is easily accessible to the person for whose use it is provided, when that person is seated.

Life Rafts and Survival Equipment - Flights over Water

602.63 (1) No person shall operate over water a single-engined aeroplane, or a multi-engined aeroplane that is unable to maintain flight with any engine failed, at more than 100 nautical miles, or the distance that can be covered in 30 minutes of flight at the cruising speed filed in the flight plan or flight itinerary, whichever distance is the lesser, from a suitable emergency landing site unless life rafts are carried on board and are sufficient in total rated capacity to accommodate all of the persons on board.

(2) Subject to subsection (3), no person shall operate over water a multi-engined aeroplane that is able to maintain flight with any engine failed at more than 200 nautical miles, or the distance that can be covered in 60 minutes of flight at the cruising speed filed in the flight plan or flight itinerary, whichever distance is the lesser, from a suitable emergency landing site unless life rafts are carried on board and are sufficient in total rated capacity to accommodate all of the persons on board.

(3) A person may operate over water a transport category aircraft that is an aeroplane, at up to 400 nautical miles, or the distance that can be covered in 120 minutes of flight at the cruising speed filed in the flight plan or flight itinerary, whichever distance is the lesser, from a suitable emergency landing site without the life rafts referred to in subsection (2) being carried on board.

(4) No person shall operate over water a single-engined helicopter, or a multi-engined helicopter that is unable to maintain flight with any engine failed, at more than 25 nautical miles, or the distance that can be covered in 15 minutes of flight at the cruising speed filed in the flight plan or flight itinerary, whichever distance is the lesser, from a suitable emergency landing site unless life rafts are carried on board and are sufficient in total rated capacity to accommodate all of the persons on board.

(5) No person shall operate over water a multi-engined helicopter that is able to maintain flight with any engine failed at more than 50 nautical miles, or the distance that can be covered in 30 minutes of flight at the cruising speed filed in the flight plan or flight itinerary, whichever distance is the lesser, from a suitable emergency landing site unless life rafts are carried on board and are sufficient in total rated capacity to accommodate all of the persons on board.

(6) The life rafts referred to in this section shall be

(a) stowed so that they are easily accessible for use in the event of a ditching;

(b) installed in conspicuously marked locations near an exit; and

(c) equipped with an attached survival kit, sufficient for the survival on water of each person on board the aircraft, given the geographical area, the season of the year and anticipated seasonal climatic variations, that provides a means for

(i) providing shelter,

(ii) providing or purifying water, and

(iii) visually signalling distress.

606.02 Liability Insurance

(1) This Section applies to every owner of an aircraft that is registered in Canada, or registered pursuant to the laws of a foreign state and operated in Canada, who is not required to subscribe for liability insurance in respect of the aircraft pursuant to Section 7 of the Air Transportation Regulations.

(2) Subject to subsection (3), none of the following aircraft owners shall operate an aircraft unless, in respect of every incident related to the operation of the aircraft, the owner has subscribed for liability insurance covering risks of injury to or death of passengers in an amount that is not less than the amount determined by multiplying $300,000 by the number of passengers on board the aircraft:

(a) an air operator;

(b) the holder of a flight training unit operator certificate; or

(c) the operator of a balloon in which fare-paying passengers are carried on board pursuant to Subpart 3.

(3) The insurance coverage referred to in subsection (2) need not extend to any passenger who

(a) is an employee of an owner referred to in paragraph (2)(a), (b) or (c), if workers' compensation legislation governing a claim for damages against the owner by the employee is applicable; or

(b) is carried on board the aircraft for the purpose of conducting a parachute descent, where the air operator has posted a readily visible notice to inform passengers, before embarking, that there is no insurance coverage for parachutists.

(4) No aircraft owner not referred to in paragraph (2)(a), (b) or (c) shall operate an aircraft of more than 2 268 kg (5,000 pounds) maximum permissible take-off weight unless the owner has, in respect of the aircraft, subscribed for liability insurance covering risks of injury to or death of passengers, other than passengers carried on board that aircraft for the purpose of conducting a parachute descent, in an amount not less than the amount determined by multiplying $300,000 by the number of passengers on board the aircraft.

(5) No aircraft owner referred to in paragraph (2)(a), (b) or (c) shall operate an aircraft unless, in respect of every incident related to the operation of the aircraft, the owner has subscribed for liability insurance covering risks of public liability in an amount that is not less than

(a) $1,000,000, where the maximum permissible take-off weight of the aircraft is not greater than 3 402 kg (7,500 pounds);

(b) $2,000,000, where the maximum permissible take-off weight of the aircraft is greater than 3 402 kg (7,500 pounds) but not greater than 8 165 kg (18,000 pounds); and

(c) where the maximum permissible take-off weight of the aircraft is greater than 8 165 kg (18,000 pounds), $2,000,000 plus an amount determined by multiplying $150 by the number of pounds by which the maximum permissible take-off weight of the aircraft exceeds 8 165 kg (18,000 pounds).

(6) No aircraft owner referred to in paragraph (2)(a), (b) or (c) shall, in order to comply with subsections (2), (4) and (5), subscribe for any liability insurance that contains an exclusion or waiver provision that reduces the insurance coverage for any incident below the applicable minimum determined pursuant to those subsections, unless that provision

(a) is a standard exclusion clause adopted by the international aviation insurance industry that applies in respect of

(i) war, hijacking and other perils,

(ii) noise, pollution and other perils, or

(iii) radioactive contamination;

(b) is in respect of a chemical drift;

(c) includes a statement that the insurance does not apply in respect of liability assumed by the owner under any contract or agreement unless the liability would have attached to the owner even in the absence of such a contract or agreement; or

(d) includes a statement that the policy is void if the owner has concealed or misrepresented any material fact or circumstance concerning the insurance or the subject thereof or if there is any fraud, attempted fraud or false statement by the owner touching any matter relating to the insurance or the subject thereof, either before or after an incident.

(7) An aircraft owner referred to in paragraph (2)(a), (b) or (c) may comply with subsections (2), (4) and (5) by subscribing for comprehensive single limit liability insurance that consists of a single policy or a combination of primary and supplementary policies.

(8) No aircraft owner not referred to in paragraph (2)(a), (b) or (c) shall operate an aircraft unless, in respect of every incident related to the operation of the aircraft, the owner has subscribed for liability insurance covering risks of public liability in an amount that is not less than

(a) $100,000, where the maximum permissible take-off weight of the aircraft is 1 043 kg (2,300 pounds) or less;

(b) $500,000, where the maximum permissible take-off weight of the aircraft is greater than 1 043 kg (2,300 pounds) but not greater than 2 268 kg (5,000 pounds);

(c) $1,000,000, where the maximum permissible take-off weight of the aircraft is greater than 2 268 kg (5,000 pounds) but not greater than 5 670 kg (12,500 pounds);

(d) $2,000,000, where the maximum permissible take-off weight of the aircraft is greater than 5 670 kg (12,500 pounds) but not greater than 34 020 kg (75,000 pounds); and

(e) $3,000,000, where the maximum permissible take-off weight of the aircraft is greater than 34 020 kg (75,000 pounds).

(9) Subject to subsection (10), no owner or operator of an aircraft shall operate the aircraft unless there is carried on board the aircraft proof that liability insurance is subscribed for in accordance with this Section.